## Slide 1: UNIT V INFORMATION THEORY
Dr.M.Manimegalai, ASP, ECE
GCE, Bargur

## Slide 2: 📡 Information Theory in Communication Systems
Information Theory is the mathematical foundation that tells us how information is measured, transmitted, compressed, and protected against noise in a communication system. It answers a core question:
What is the maximum amount of information that can be sent reliably over a channel?
🔷 Why Information Theory is Needed
In real communication systems:
  Signals are corrupted by noise
  Bandwidth and power are limited
  Errors cannot be avoided completely
Information theory helps us:
  Quantify information content
  Determine maximum achievable data rate
  Design efficient coding and modulation schemes
  Analyze error performance limits

## Slide 3: 🔹 Information Source
📌 Definition
An information source is the origin of the message in a communication system.
It produces symbols or messages that convey information to be transmitted.
👉 In simple words: Information source = where the message comes from
🔹 Discrete Memoryless Source (DMS)
A Discrete Memoryless Source (DMS) is an information source that:
  Produces discrete symbols
  Has no memory of past symbols
  Generates each symbol independently with fixed probabilities
👉 The probability of the current symbol does not depend on previous symbols.

## Slide 4: What is Information
Information is a quantitative measure of uncertainty associated with a random event.
1️⃣ Information
  Information is related to uncertainty
  Rare events carry more information
An event carries more information if it is less likely to occur.
Mathematically, the information content of an event is:

## Slide 11: 🔹 Entropy (H)
📌 Definition
Entropy is the average amount of information produced by an information source. It measures the uncertainty or randomness of the source.
👉 More uncertainty → higher entropy 👉 More predictability → lower entropy

## Slide 21: Joint Entropy
In a communication system, joint entropy explains how much total information (or uncertainty) is associated with the transmitted message and the received message taken together.

## Slide 25: Conditional Entropy
Conditional entropy measures the average uncertainty remaining in one random variable when another random variable is known.